## Slide 1: From Dafny to RTL
Dafny
requires/ensures verified
Vitis HLS
C synthesis → reports
Refactor for HLS
fixed-size types + remove runtime functions
Dafny → C++
top.cpp + runtime
Verilog RTL
FSM + MUX + comparator logic

## Slide 2: Abstraction to Hardware

## Slide 3: HLS Synthesis Results
Metric | Value
Latency | 9 cycles (90 ns)
Interval | 10 cycles
Slack | 3.02 ns
LUT | 185 (2%)
FF | 109 (~0%)
DSP | 0
BRAM | 0
Metric | Value
Latency | 1 cycles (10ns)
Interval | 2 cycles
Slack | 2.70 ns
LUT | 585 (7.3%)
FF | 286 (1.8%)
DSP | 0
BRAM | 0
Normal:
UNROLL:

## Slide 4: RTL Analysis
ap_start: trigger one transaction
ap_done: asserts when complete
ap_idle: high when waiting start
ap_ready: indicates readiness for next
Control Path：
2 Small State Machine
setlt → comparator (max < v)
select → mux (choose larger value)
add → loop counter increment
1 Comparator 1 Mux 1 Adder

## Slide 5
Sequential Compare-and-Update Logic：
Single comparator reused
Mux-based value selection
Max stored in register
Loop controlled by scheduler
Normal Version:
“#pragma HLS UNROLL” Version: (AI Recommend) :
The absence of unrolling results in a time-multiplexed datapath rather than a spatially expanded comparator network.